## Slide 1: SELF DRIVING CARS USING CNN Batch Name : BDAROOS
Sravani Niharika Garapati (16328843)
Nikhila Chirumamilla (16323180)
Sai Ram Chaganti (16328843)
Shravani Nalla(16328843)

## Slide 2: Table of Contents
Introduction
Why self driving cars
Companies Investing in Self Driving Cars
Related Works and Leaders in the innovation
Data Collection and Manipulation
Approach Used: Neural Networks
Architecture
Software Requirements
Model Training
Results
Conclusion
Future Scope
References

## Slide 3: Introduction
Self driving cars, one of the trending topics all over the world. A car with no steering wheel, pedals and with the most advanced technology autopilot.
A Self driving car, also known as autonomous vehicle(AV), is a car incorporating vehicle automation, that is a ground vehicle that is capable of sensing its environment and moving safely with little or no human input.
In our project, we will be using an advanced neural network in combination with Computer vision to build a self driving car.
It learns the whole set of algorithms required to operate a car's steering wheel.
In a simulated driving situation, the CNN was trained and evaluated using data.
A front-facing center camera footage may be used to generate control orders for the car's steering once it has been trained.

## Slide 4: Why self driving cars
Below are the main reasons why we need self driving cars
90% reduction in traffic deaths
60% drop in harmful emissions
Eliminate stop and go waits by 100%
10% improvement in fuel economy
500% increase in lane capacity
40% reduction in travel time
Consumer savings of £5bn
Greater Independence

## Slide 5: Companies Investing in Self Driving Cars

## Slide 6: Related Works and Leaders in the Innovation
Waymo
Previously owned by the GOOGLE
Tesla
Already rolling out self-driving cars
Waymo and Tesla are considered to be the leaders in the innovation of self-driving cars
Waymo and Tesla use a variety of sensors and cameras to construct a 3D representation of the car's surroundings.
A 360-degree representation of the environment requires expensive technology like as LIDAR , radar and ultrasonic sensors
the Tesla Model S makes use of a single back camera as well as broad and narrow front cameras that view within.
Twelve ultrasonic sensors in the back, plus a RADAR in the front, allow the automobile to measure the speed of things in front of it.

## Slide 7: jksx
Methodology

## Slide 8: Data Collection and Manipulation
The goal is to forecast the steering wheel movements of a self-driving automobile based on data from a camera in front of the vehicle.
There are two modes in system’s operations
1)Data Collection Mode
2)Self Driving Mode
To train the neural network, depiction of the steering wheel angle neural network, the camera records its pictures and sensors measurements. The camera inputs pictures straight into the neural network while our system is driving the automobile.
To begin gathering data, we must first alter the surrounding environment to our favor. On various courses with sharp and smooth curves, bumps, trees and traffic signals, the simulated cameras deliver views in front of the car.
A background script gathers information on the driver's control of the steering wheel, throttle, and brake pedals.
The photos captured by the camera are processed before they are sent to the network.

## Slide 9: Data Collection and Manipulation(Contd..)
There are various steps before images from the camera are sent to the network:
Selection procedure: data with desirable qualities is picked and separated into a training and a validation set, the training set consisting of 80% and the validation set consisting of 20% of the data.
Changing the color scheme of the input photos may be accomplished via the use of the color scheme modification technique.
The photos are then cropped to eliminate the front of the automobile, resized to 66x20, and converted from RGB to YUV since YUV takes into consideration human perception, enabling decreased bandwidth for chrominance components.
Afterwards, the pictures are supplemented by adding simulated shifting and rotations to teach the network how to recover from a bad location or orientation. Using a normal distribution with a mean of 0, the magnitude of each of these disturbances is generated at random.
The last step is to combine the pictures along with their related steering angel, throttle, and brake values and feed to neural networks as arrays.

## Slide 10: Approach: Neural Networks
Neural Networks employ numerical vectors or matrices as input and conduct operations like additions and matrix multiplication, such as matrix multiplication to control the parameters.
In order to provide output for the next layer, activation functions require weights, biases, and a specified input.
The findings are shown on the output layer, which is the last stage of the pipeline.
For each input, the difference between the calculated and intended output is specified by a loss function.
The optimizer in a neural network is used to minimize the discrepancy between predicted and actual results.
For training, an optimization strategy starts with a random set of weights.
Additional layer types and connections between layers are needed to create an array of neural and deep network architectures.

## Slide 11: Architecture
Feed forward neural networks and backward neural networks were the two NN architectural types we employed in our tests.
First, images with dimensions of 160X320X3 are used as input, followed by five convolution layers with 24, 36, 48, 64, 64 neurons in each, each with a filter size of 5X5 and a 2X2 pixel jump at each filter pass (strides of sizes 2X2), and two final layers with filter sizes of 3X3 but no strides.
The final two layers use filter sizes of 3X3 but no strides. Once the convolutional layers have produced their multi-dimensional output, they are followed by a flattening layer.
There are 5 layers in total each with 100 neurons
Activation Function Used: Relu
Optimizer Used: Adam
Model Used : Sequential
Batch size ranges from 100 to 200
Number of time periods :10
Steps-per-epoch: 300.

## Slide 12: Architecture(Contd..)
Consider the below architecture model

## Slide 13: Software Requirements
Simulator
TensorFlow
Keras
SocketIO
Flask
Opency
Pillow

## Slide 14: Model Training
Once the information has been gathered and analyzed, there are 600 random samples chosen from CSV, and the network is trained on the training set by drawing random batches until the whole training set has been utilized, then drawing random batches again. The network is tested against the validation set at regular intervals
We upload the data to a Google Drive account and attach it to Google Colab before we begin training. After that, Colab is utilized to get the training started.
Using a batch generator and a model with random weights, input batches are fed into the system before being sent through the layers and compared to the provided labels.
The Adam optimizer adjusts the weights after computing the output's mean square error via the back propagation procedure.
The validation loss is calculated and recorded after each run through the inputs in the first epoch check point function, and if the following epoch yielded a lower value for the validation loss, a copy of the model and its associated weights are saved as model.h5 file.
Model.h5 file is created to save the weights for future testing and operation of the self-driving automobile when all the epochs have been completed.

## Slide 15: Results

## Slide 16: Conclusion
This research reveals that CNN can be taught using simulation data to run autonomous automobiles. We found that CNNs can learn the whole lane and road follow job without the need for human breakdown into lane recognition, semantic abstraction, route planning and control. Deep Neural Networks and classic computer vision methods were used in this study to see whether they might lessen risky driving behavior in self-driving cars. The process of setting up the investigation's environment and assembling the tools required a significant amount of time throughout development. Future autonomous driving initiatives will benefit tremendously from using a system that blends classic computer vision methods with the processing power of DNNs, according to the study.

## Slide 17: Future Scope
It's recommended that we collect additional training data in a variety of lighting settings to improve the CNN's capabilities. Definitely this will increase the precision of the car's navigation system. It is also possible to enhance the model's functionality by adding features such as the ability to avoid obstacles encountered on the course. An accurate model might benefit greatly by the CNN being implemented on a real automobile.

## Slide 18: References
[1] G. Eason, B. Noble, and I. N. Sneddon, “On certain integrals of Lipschitz-Hankel type involving products of Bessel functions,” Phil. Trans. Roy. Soc. London, vol. A247, pp. 529–551, April 1955. (references)
[2] J. Clerk Maxwell, A Treatise on Electricity and Magnetism, 3rd ed., vol. 2. Oxford: Clarendon, 1892, pp.68–73.
[3] I. S. Jacobs and C. P. Bean, “Fine particles, thin films and exchange anisotropy,” in Magnetism, vol. III, G. T. Rado and H. Suhl, Eds. New York: Academic, 1963, pp. 271–350.
[4] K. Elissa, “Title of paper if known,” unpublished.
[5] R. Nicole, “Title of paper with only first word capitalized,” J. Name Stand. Abbrev., in press.
[6] Y. Yorozu, M. Hirano, K. Oka, and Y. Tagawa, “Electron spectroscopy studies on magneto-optical media and plastic substrate interface,” IEEE Transl. J. Magn. Japan, vol. 2, pp. 740–741, August 1987 [Digests 9th Annual Conf. Magnetics Japan, p. 301, 1982].
[7] M. Young, The Technical Writer’s Handbook. Mill Valley, CA: University Science, 1989.